ESP32 CW Trainer — WiFi Setup Guide

This CW Trainer has two functional modes. The default mode is as a CW Trainer implemented as a Koch method training device. As a trainer, the ESP32 sends CW for characters and asks the user to recognize the characters.

The second functional mode is as an Iambic Keyer. Six memories are implemented for preset messaging. GPIO pin 18 selects this functionality.

Iambic Keyer
GPIO 18	Mode
Logic HIGH / (float open)	CW Trainer
Logic LOW / (ground)	Iambic Keyer

GPIO Pin 19 selects the ESP32 boot mode: either AP or Wifi STA. This switch is read once at boot. A switch change and reboot and is required when changing modes.

Switch 3 Mode Selector Position
GPIO 19	Mode
Logic HIGH / (float open)	AP
Logical LOW / (ground)	STA

AP Mode (Default) — ESP32 creates its own network, so no internet. User interface is http running Java Script on a browser or serial terminal. First time setup relies on user to provide login credentials. Subsequent connections are automatic.

Step 1 — Power on the ESP32 with GPIO19 pin open or unconnected.

Step 2 — On your phone or computer, connect to this WiFi network:

AP Mode
Network name (SSID)	ESP32_Morse_Trainer
Password	morse1234

Step 3 — Open a browser, enter this URL and go to: http://192.168.4.1 If your device supports mDNS, use alternate http://cwtrainer.local

Step 4 — The blue LED (ESP32 GPIO pin 2) on the board lights solid when the AP is active and blinks briefly each time a device connects. Up to 4 devices can connect simultaneously, but be mindful of the thermal load.

<<<>>>

STA Mode — ESP32 joins an existing WiFi network. User interface is HTTP running Java Script on a browser or serial terminal. First time setup relies on user to provide login credentials. Subsequent connections are automatic.

First-Time Setup

Step 1 — Log into a local WiFi AP before powering on the ESP32. This might be your local computer network board connected to a local WiFi network, or it might be a hotspot on your phone or other device. Your home WiFi network should already be active if you are connecting to that.

Step 2 — Power on the ESP32 with GPIO pin 19 grounded (STA Mode).

Step 3 — On a separate device (laptop or second phone), connect to the temporary setup network:

STA Mode
Network name (SSID)	CW_Trainer_Setup
Password	morse1234

Step 4 — A captive portal page opens automatically. If it does not, browse to 192.168.4.1

Step 5 — In the portal, select your network’s name and enter its password. Submit. These credentials are saved securely on the ESP32 and provided automatically for subsequent logins.

Step 6 — The ESP32 connects and prints its assigned IP to the Serial monitor:

    ✓ Connected to hotspot!      IP Address: 192.168.x.x

Step 7 — On your phone, browse to that IP address, or use this URL

http://cwtrainer.local

Subsequent Boots

Credentials are saved. The ESP32 connects automatically within ~15 seconds. No portal is needed unless the network changes.

If the portal times out (3-minute window): the ESP32 retries saved credentials in the background. Reboot the ESP32 to reopen the portal and enter credentials.

<<<>>>

Changing Modes

1.	Flip the physical switch on pin 19 to the desired mode (AP or STA).
2.	Reboot the ESP32
3.	Confirm in the Serial monitor “Status” option:

    WiFi mode: AP (ESP32 hotspot access for your browser), or
    WiFi mode: STA (phone wifi or home wifi browser access)

Signal Strength Warning (STA Mode)

Use the “wifi show” command in the serial port for this information. Show the command menu by sending help to the ESP32 through the serial port.

Signal Strength
RSSI	Status
Better than −75 dBm	Good
−75 to −85 dBm	Weak — may drop occasionally
Worse than −85 dBm	Unreliable — use AP mode instead

<<<>>>

Two questions about this Morse Trainer as implemented:

Is it ever necessary for the operator of the Trainer to know the Trainer device's IP address when logging on in STA (station) mode? Or, is the IP address that of the WiFi network to which this Trainer logs onto? If the Trainer operator needs to know the Trainer's IP address in order to log on, how would you suggest implementing that?

What onboard module firmware and hardware is used by this Trainer in both its AP and STA modes? These operating modes run separately, never consecutively, but do they use the same esp32 resources?

Here are answers based on typical ESP32 Morse Trainer implementations:

Is it ever necessary for the operator of the Trainer to know the Trainer device's IP address when logging on in STA (station) mode?
- Yes, in STA mode, the ESP32 connects to an existing WiFi network and is assigned an IP address by the router. If the operator wants to access a web interface or service hosted by the Trainer, they need to know the ESP32’s assigned IP address (not the router’s IP).
- To display the Trainer’s IP address, you can:
- Print it to the serial console (Serial.println(WiFi.localIP());).
- Show it on an attached display (OLED, LCD, etc.).
- Blink it out in Morse code using an LED.
- Use mDNS (e.g., esp32.local) for easier access if supported.

What onboard module firmware and hardware is used by this Trainer in both its AP and STA modes?
- Both AP (Access Point) and STA (Station) modes use the ESP32’s built-in WiFi hardware and the ESP-IDF or Arduino core WiFi libraries.
- The same WiFi radio and firmware resources are used for both modes, but the configuration changes:
- In AP mode, the ESP32 creates its own WiFi network for clients to join.
- In STA mode, the ESP32 joins an existing WiFi network.
- The modes are mutually exclusive in your implementation (never run at the same time), but they use the same underlying ESP32 WiFi hardware and software stack.

<<<>>>

Changes made:

1. Added pin definitions:
  1. IP_BLINK_SWITCH_PIN = 15 (INPUT_PULLUP, active LOW)
  2. EXTERNAL_LED_PIN = 16 (OUTPUT)
2. Added Morse timing constants for 10 WPM (120ms dit)
3. Added Morse code lookup tables for digits 0-9, letters N/C, and period
4. Implemented functions:
  1. checkIPBlinkSwitch() - Polls the switch with debouncing
  2. blinkIPAddress() - Blinks the full IP address if connected
  3. blinkNC() - Blinks "NC" three times if not connected
  4. blinkMorseCode() - Low-level function to blink any Morse string on both LEDs
5. Integrated into loop():
  1. Only checks the switch when in STA mode (else block after checkWiFiSTA())
6. Behavior:
  1. In STA mode, when GPIO15 is grounded, the trainer checks if connected
  2. If connected: blinks IP address (e.g., 192.168.1.100)
  3. Uses both the onboard LED (GPIO2) and external LED (GPIO16)

Hardware connections:

- Connect a momentary switch between GPIO15 and GND
- Connect an LED (with current-limiting resistor) between GPIO16 and GND

Key changes:

1. checkIPBlinkSwitch() now uses a while loop that continues as long as GPIO15 is LOW
2. Repeatedly blinks IP address (if connected) or NC (if not connected)
3. Checks switch state during blinking to allow early exit if released
4. 1-second pause between repetitions for readability
5. Early exit checks in blinkIPAddress(), blinkNC(), and blinkMorseCode() to stop immediately when switch is released

Behavior:
- Hold GPIO15 to ground → blinks continuously
- If not connected: "NC NC NC..." repeats
- If connected: "192.168.1.100 192.168.1.100..." repeats
- Release switch → stops immediately and returns to normal operation