ESP32 Morse Code Trainer Quick Start
Part 1 — Phone / iPad / Browser Access
1. Connect to WiFi
  •	AP mode: connect to ESP32_Morse_Trainer
  •	Password: morse1234
  •	Open http://192.168.4.1 or http://cwtrainer.local
  •	STA mode: connect the trainer to your hotspot/network first
  •	If setup is needed, join CW_Trainer_Setup
  •	Password: morse1234
  •	Then open http://cwtrainer.local or the trainer IP
2. Morse Code Trainer
  •	Put the mode switch in Trainer
  •	Open the web page
  •	Start Koch or Echo training
  •	In Koch mode, tap/type the character you hear
  •	Adjust speed, buzzer, and key type from the web UI
3. Memory Keyer
  •	Put the mode switch in CW Keyer
  •	Open the web page
  •	Enter text into memory slots M1–M6 •	Save the message
  •	Press Play to transmit it
  •	Memory playback works only in CW Keyer mode

Part 2 — Serial Monitor Access
1. Connect 47
  •	Open the serial monitor at 115200 baud
  •	Power up the unit
  •	Use help to show commands
2. WiFi Setup
  •	Show WiFi status: wifi show
  •	Clear saved STA credentials: wifi reset
3. Morse Code Trainer
  •	Set Trainer mode with the hardware switch
  •	Useful commands:
  •	koch start
  •	koch pause
  •	koch resume
  •	koch stop
  •	koch stat
  •	echo start
  •	echo stop
  •	key straight
  •	key iambic
  •	wpm 18
  •	buzzer on
4. Memory Keyer
  •	Set CW Keyer mode with the hardware switch
  •	Check status with keyer
  •	Set speed with wpm XX
  •	Memory storage/playback is primarily controlled from the web page
5. Quick Check
  •	status shows current settings
  •	help shows all commands
If needed, a one-page printable version can be condensed further.